Water Tank Electromagnetic Interference Problem Log

During my time establishing the infrastructure of my water tank control system I came about a particular problem where my strain gauge sensor would occasionally give incorrect values. This document serves as a log on my troubleshooting journey to correct the issue.

I have collected data from the strain sensor whenever my system was running with a water pump and in various under configurations and labeled them in the format of “data-<month-day-year>--<hour-minute-second>”. Below is some analysis with the data I collected.

Note: In all cases the strain data errors only occur when a water pump was actually drawing current (particularly around 300 mA).

“data-2-8-2023–14-2-38”:
This entry will serve as a basis in analysis. In this case I had two Arduino’s one I called the “pump Arduino” and the other the “scale Arduino”. Both Arduino’s were on the same level on top of the wooden structure inside a plastic box attached with Velcro. In this setup, the scale Arduino fed power to the scale sensor and was not coupled with the power rail of the pump Arduino. For some reason this decoupling makes a difference in the quality of the scale sensor readings. Presumably because in order to couple the two the wire most cross the PWM signal generated by the pump Arduino which introduces small noise to the scale power line. The algorithm I created was not used in this entry. This data entry has the best error percentage ever observed at 0.0662%.

Building off the prior entry are entries which introduce capacitors into the systems circuits. Below are the results.

“data-2-8-2023–13-50-39”:
In this test run the algorithm is disabled and introduces a 47 uF capacitor on the pump Arduino power rail. The error percentage was 0.1370%.

“data-2-8-2023–14-13-27”:
Same as entry “data-2-8-2023–14-2-38” except the scale power came from being coupled with the pump Arduino power rail. The error percentage was 2.6567%.

“data-2-8-2023–14-21-9”: Same as prior entry except the 47 uF capacitor on the pump Arduino power rail tried in “data-2-8-2023–14-50-39” was introduced. The error percentage was 2.6923%.

An interesting thing can be concluded from going from “data-2-8-2023–14-2-38” to “data-2-8-2023–13-50-39” and “data-2-8-2023–14-13-27” to “data-2-8-2023–14-21-9” is that adding a bypass capacitor on the power rail did not assist the strain gauge error and actually increased it slightly.
Another conclusion is that it is not a good idea to couple the power of the scale sensor with the power rail of the pump Arduino, not necessarily because the power line has ripples (the addition of the capacitor would have fixed this if it were the case), but likely the introduced EMI (electromagnetic interference) that comes with having the scale power wire be close to other noisy wires on the same breadboard. There exists an entry “data-2-8-2023–14-56-22” which has the scale sensor’s power decoupled from the pump Arduino's power rail, but still on the same breadboard. The error percentage found was 5.2181%. This means that it isn’t the sharing of the power rail that is necessarily the issue but all the noise in the region that comes with doing so that is the problem.
“data-2-8-2023–15-2-59”: essentially a second trial of the really low error case that occurred in “data-2-8-2023–14-2-38” that had obtained an error percentage of 0.3989%. This supports that the low error case was not just a fluke. (Note: This data just has the rising strain portion and makes the percentage higher than it should be)

“data-2-8-2023–15-32-34”: at this point the two Arduino’s were physically separated from search other. This put the strain Arduino farther away from the pump Arduino in the hopes of reducing the noise on the strain sensor from the second Arduino. The error percentage was 0.2066%.

On 2-12-2023 I had done some experimenting with Faraday fabric. While its EMI blocking capabilities do work as when I applied it to wrap up the scale Arduino, the results were not satisfactory enough. My present suspicions are that the motor driver and the power lines are interfering a bit with the pump Arduino and breadboard and causing the EMI to be carried by the wires to the scale Arduino. My next approach will be carefully wrapping the motor driver with Faraday wrap and possibly raising the breadboard and pump Arduino up again, but perhaps adding Faraday wrap to shield the scale Arduino and scale sensor the EMI that will reintroduce. I have ordered an EMF meter and will be using that in my decisions when it arrives.