Water Tank Digital Control System Project

Background:
This project has been one that I had been wanting to do for a long while ever since I had taken my first control system classes in college. Due to various obligations, such as taking Electrical Engineering courses which do not immediately pertain to control theory / control systems, and already being in charge of researching and developing software for unmanned air vehicles (UAVs) as a college senior design project I was not able to get this water tank project started to deepen my understanding of control theory. However, despite not being able to start on this project as soon I would have liked, partaking in the UAV senior design project did reintroduce me to the world of programming which I had only dabbled in my freshman or perhaps sophomore year of college in a single course of C++ in an integrated development environment (IDE). I learned how to not be spooked by the terminal, notably due to having to use/learn Linux (Ubuntu specifically), learned how to start programming in Python (3.x specifically), and began to be more able to read dense programming documentation which assumes understanding of object-orientated programming. After having recently graduated around December 23, 2022 I began to learn more C++ and reread / relearned old linear systems / control theory material that I had studied at one point, but had forgotten / went over my head the first go around.

Development:
Arduino developments started off as simple tests to review/learn how to incorporate potentiometers, buttons. Soon after external libraries and hardware were incorporated and experimentation in getting data from a strain sensor/controlling a water pump through a motor driver. Those skills I obtained from the UAV project carried over in my water tank project where a Python program was developed to be able to intake data from an Arduino via USB and to organize and store it as a “.mat” file that MATLAB can use. The data transmitted over the wire is strain, valve, and time values in “serial_receiver.py” with setpoint values being included in “serial_receiver_v2.py”. In addition, the MATLAB programming skills I learned throughout college and self research came in to allow me to be able to analyze the data gathered and stored by the Python programs. First, by filtering stacked samples (have multiple sample values at a given instance of time) followed by then plotting the data, and subsequently performing deeper control system specific analysis. That would include system identification, Simulink, and PID design. I would have liked to say that the project went as smoothly as it so far seems, but that is not the case.

 Difficulties:
Serial Communication:
One of the first setbacks that held the project back early on was the correct implementation of serial communication. Despite not having a computer science background, and hence not knowing all the important nonphysical details on how computers accomplish their various tasks I was able to construct a mental model of how serial communication seems to work based on test programs I had made to get a better understanding. The mental model is that whenever two machines want to communicate, in this case via USB, that practically there will have to exist some chunk of memory dedicated to the task in the event of the very real possibility of some fluctuation of data transfer rate. Allow me to explain, ideally if two machines are communicating at say X bits per seconds then whenever machine A sends something to machine B then it used immediately. The process of machine A sending a bit to machine B can be approximately as occurring instantaneously over the wire once sent, but that is not to say that its usage is instantaneous as well. Computers, specifically those of personal computers that use general purpose operating systems (OS) like standard Windows, MacOS, and Linux will not be so strict to maintain a clockwork relationship for its various computer obligations (processes) such as using the data it has been sent by another machine. As a result it becomes necessary to have a sort of holding cell where data can sit and wait for a moment until the OS gain the capacity to process the waiting data and make room for more data to enter. If the holding cell more appropriately called a “buffer” gets full then the possibility of messages getting sliced when they are longer than the remaining buffer space can occur. The ruining of data is what is called “corruption”. This was learned by me in that whenever an Arduino is allowed to indefinitely generate data over the wire and I tried starting up my Python script to process the data that sometimes the Python script would get jammed in the beginning due to garbage (corrupted) data. It would only be after a couple of revs (a kin to revving up a lawn mover) that it would properly start up presumably due to the “top” portion the buffer being cleaned of the scum (corrupted) data. From this experience, it was learned the importance of utilizing the functions/methods that monitor the state of the buffers and that it was more robust in my project to have redesign the Python script so that it is always listens on the line and processes the buffer when data arrives and to have the Arduino start generating that data after a push of a button. In this manner the problems encountered with implementing serial communication were resolved, and never occurred in the project again after that.

Electromagnetic Interference:
The prior problem was one that was purly software based, the next problem was one that was purely hardware based and much more persistent. After much time consuming testing, and attempted remedies it was conclusively found that the reason why in this project there was instances where horrifically inaccurate data was generated was due electromagnetic interference (EMI). Allow me to explain, strain gauges are sensors that correlates resistance to material strain. The change in resistance is very subtle and requires some electrical engineering trickery by implementing a special circuit configuration called a Wheatstone bridge. Without going much into detail, the Wheatstone bridge effectively allows for measurement of the subtle resistance changes with more practical voltage that can then after be amplified. However, given the nature of subtly in the measurement the sensor highly susceptible to change in the environment. Be it temperature change which affects the resistance created by the strain sensor, or in my case the EMI coming from my system which presumably affects the balance of the Wheatstone and generates erroneous data for a moment. The source of the EMI was mainly due to my DC electrical motor (liquid pump) that was having its strength managed through a high current pulse width modulated (PWM) signal. PWM signals, particularly those of high current are incredibly noisy due to the high frequency content contained when a signal quickly swaps and forms a rising edge. A purchase and usage of and EMF meter confirmed this as the motor was generating around 350 V/m ~ 400 V/m at full power (around 300 mA with 490 Hz PWM signal). While 350 V/m ~ 400 V/m may or may not be much EMF (I would not know, I was never particularly interested in antennas) that level of EMF was enough to interfere with the strain gauge measurements as that sensor is highly sensitive to noise in the environment. There exists two options, either move the motor farther away from the strain gauge sensor (which come with the cost of needing a more powerful motor to move the water from farther away which comes with more EMF generation), or to simply shutoff the motor for a moment and take the sample measurement followed by turning the motor back on at the desired strength. (Note: Faraday fabric was tried on both the wrapping the strain sensor and then the motor / power supply, but was not sufficient as the EMF was quite strong as well as not being possible to perfectly wrap the things in the fabric leading to EMF leakage and then EMI. The workaround of turning the motor off for a moment to make a sample and then turning it back on was chosen and utilized as moving the motor and buying a more powerful motor was not an option I was willing to make. After this design decision the project continued to move forward after being jammed for quite some time with the EMI problem.

System Identification and PID Controller Design:
This is issue was about the quickest to resolve, but posed some difficulties as system identification and PID controller design were seldom discussed in my college control system classes due to lack of time. One of the first issues encountered with system identification is deciding how complicated the model of the transfer function should be to maintain decent accuracy, but not so complicated that it made PID design (even with the PID tuner MATLAB app) to be difficult and produce unsatisfactory results. Another issue observed with transfer functions initalially developed is that when tested in simulink the mode assumes that certain values accuation signals were valid and would produce a real output which is not the case. What is meant by this is that there exists a region of liquid pump strength where the motor is incapable of successfully dropping water into the tank. In other words, there exists a lower bound. In order for this to not interfere in the design of a PID controller, data was recollected after reprogramming the embedded system to operate only between the lower bound where the motor is barely not able to bring water into the tank to maximum power that the liquid pump was capable of. This allowed for being able to make a simpler and decently accurate plant transfer function model that would actually be representative of what accusation signals could actually exist in the real system. Regarding PID design there were not much difficulties. It was found that for up to a PI controller the equation provided by MATLAB when converted to the standard form of a Z-transform equation matched very closely, whereas the PID with filtered derivative term had substantial deviation. However, this discrepancy was observed at the time a complicated and borderline marginally stable / unstable transfer function was being used which is likely responsible. In the current writing of this log, only a P controller was actually implemented into the real system as it was simple and I was satisfied with the small steady state error the system had. Perhaps in the future PI and PID may be experimented with as well, but for now the project has been plenty successful and satisfactory to me.